## Slide 1
OPERATING
SITUATION
MONITORING
MONITORING
FREQUENCY
NSR AND TV: VOC/HAP LDAR FUGITIVES MONITORING
VERSION: April 19, 2017
25 & < 100 TPY Facility Wide Fugitives
Quarterly and 15 Days
After Maintenance/
Repairs that Affect
Components
Permittee requests limits on fugitives when they are not required by the protocol or a limit is needed to avoid an applicability threshold
100 TPY Facility Wide Fugitives
Leak Detection and
Repair Program for
Specific Emission Units tailored after NSPS VV
OR
A Dept. approved enforceable condition proposed by the applicant to demonstrate compliance with a limit on Fugitives
NOTE 1: Source categories addressed by federal LDAR regulations are the following: Synthetic organic chemicals manufacturing industry plants (NSPS VV, VVa), Petroleum Refineries (NSPS GGG, GGGa, MACT CC), Natural Gas Processing Plants (NSPS KKK, OOOO, OOOOa, MACT HH). Requirements for components at well sites and compressor stations (see 40 CFR §60.5365a(i) & (j)) do not follow the general leak detection protocol based on NSPS VV, thus are not included in this definition.
Quarterly and 15 Days
After Maintenance/
Repairs that Affect
Components
None
<25 TPY Facility Wide Fugitives
None, no emission limit established
As required by LDAR regulation(s), including but not limited to: NSPS VV, VVa, GGG, GGGa, KKK, OOOO, OOOOa and/or
MACT CC, HH
NSPS / MACT: As required by regulation
Process unit(s) subject to NSPS and/or MACT
Portions OR entire facility NOT subject to
NSPS and/or MACT LDAR regulation(s)
Portions OR entire facility subject to
NSPS and/or MACT LDAR regulation(s)
Leak Detection and
Repair Program for
Specific Emission Units tailored after NSPS VV
OR
A Dept. approved enforceable condition proposed by the applicant to demonstrate compliance with a limit on Fugitives
Any source category
Source categories addressed by federal LDAR regulations
APPLICABILITY
Any source category
TV Major Source: NSR permit requirement OR source categories addressed by federal LDAR regulations1 and TV Major for VOCs
A
B
C
D
E
Leak Detection and
Repair Program for
Specific Emission Units tailored after NSPS VV
OR
A Dept. approved enforceable condition proposed by the applicant to demonstrate compliance with a limit on Fugitives
Annual and 15 Days
After Maintenance/
Repairs that Affect
Components